## Slide 1
In partnership with
Presented by Andrea, Han, Hannah, Keith, Mark, and Ying on behalf of Seattle University
Inventory Optimization
Ying

## Slide 2
Recommendations
Recommendation | Annual Savings
Eliminate deadstock | $33,000
Reduce over-ordering | $44,000
Adopt EOQ model for distribution management | $350,000
Ying
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 3
Lancaster Today: Overview
Ying
Metric | Value
Regional fill rate | 95.4% representing $1.1M in rhit costs
Storage space | 250,000 ft3 representing $1.4M in annual storage costs
Days on hand | 171 days for currently stocked items
Standard lead time | 46 days
Storage space is the key limiting factor for Lancaster, according to Paccar parts employees
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 4
Lancaster Today: Long Product Tail
Lancaster’s long product tail indicates the potential to save on stocking of low-velocity items by sourcing nationally to aggregate demand across the US
Chart: 
| revenue
1 | 1646601877.2
2 | 960540180.9
3 | 1365199343.6
9 | 573323775.3
Chart: 
| Count
1 | 13790
2 | 18774
3 | 81092
9 | 127100
The top 15% of products generate >50% of all (estimated) revenue
- FY 2018 -
High-velocity products, 15%
High-velocity products,
57%
Number of products
Revenue
Low-velocity products
Low-velocity products
Ying
* Calculations assume that revenue is proportional to cost
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 5
Eliminate Deadstock
Of the total 250,000 cubic feet of space, 6,000 cubic feet are wasted on products that have not been ordered in over 2 years
None of these items are protected, and thus can be removed relatively easily
Chart: 
| Dead stock | Stock
cubic feet of storage | 5750 | 244250
Deadstock represents 2.4% of total storage costs, or $33,000 annually
Han
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 6
Causes of over-ordering:
Paccar Parts can save up to 3.2% of Lancaster’s total storage space, or
$44K
by reducing over-forecasting and over-ordering
1
1
2
Forecasts overshoot demand by 17% overall
Ordering overshoots forecast by 16% overall
Over-Ordering
Hannah
Chart: 
| Low Velocity Products | Medium Velocity Products | High Velocity Products | Highest Velocity Products
Series 1 | 0.013 | 0.182 | 0.252 | 0.122
Ordering Overshoot of Forecast
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 7
Economic Order Quantity (EOQ) Model
The EOQ model is an optimization model used to minimize the total variable cost (TVC) of the inventory.
Optimization
Assumptions
TVC = Storage Cost + Rhit costs
Safety stock storage is a fixed cost.
Single Echelon model that does not consider other DC’s.
Demand is assumed to be constant over time.
The current TVC was calculated under the assumption that the current state of the DC is representative of the yearly state.
Mark
Output
TVC
When and how much to order for each dim
Example: order 10 windshields every two weeks instead of 25 windshields every month.
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 8
Impact of EOQ
Chart: 
| Current | EOQ
Series 1 | 1537067 | 1184923
Column1 | 352144
Adopting the EOQ model saves $350K in total variable costs
$350K/year in savings using EOQ stocking model
Total variable cost, optimized under EOQ model.
However, yearly average fill rate decreases to approximately 90%.
Savings
Mark
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 9
Next Steps: Implementation
Implement forecasting model
Apply our EOQ model to Paccar Parts’ purchase process
Quantify impact to regional fills
Machine Learning Applications
Additional analysis to determine best machine learning models
Test on a small scale (Lancaster only) before adopting nationwide
1
2
Keith
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 10
Implementing Additional Technologies
Internet of Things
Blockchain
Weather forecast data
Leverages data from sensors to identify when replacement parts are needed
Enables sharing real time insights with suppliers as necessary
Can be used to adjust stocking strategy for items that are affected by severe weather
Marginal benefit relative to cost needs to be assessed
Need to design a data transparency and security model
Limited lead time to act on weather forecast information
Keith
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 11
Disruptors: Driver Shortage
Current impacts:
Higher ground transportation costs
Potential timeliness issues
Long-term:
Slight offset to risk of recession: recession reduces demand & therefore cost of drivers
Autonomous driving
Model inclusion:
Captures regional differences in delivery costs due to driver shortages
Impact: identify unprofitable customers (remote locations, etc.)
Source: American Trucking Association
Chart: Historical Driver Shortages
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Series 1 | 15000 | 20000 | 38000 | 43000 | 35000 | 50000 | 60000
Annie
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 12
Project Review
Highlights
Work with a real data set
Focus on a single distribution facility (given stringent time frame)
Exhaustive data dictionary
Difficulties
Many data fields; could calculate them ourselves and reduce the provided number of variables without losing information
Inferring goal of Lancaster distribution hub (lack of space)
Annie
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps

## Slide 13
Questions
Thank you
We would like to take this opportunity to answer any audience questions
Annie
Notes: We explored several types of interactions, used a combined approach of first, last, linear
Overview of recommendations
Overview of next steps